## Slide 1: Water Quality parameters
Commonly used to determine the conditions of a stream

## Slide 2: 8 water Quality Parameters
Dissolved oxygen
Water Temperature
pH
Total phosphate PO4 ions
Nitrate ions / Ammonia
Turbidity
Total Dissolved Solids
Conductivity

## Slide 3: Dissolved Oxygen
Dissolved Oxygen (DO measured in ppm or mg/L or % Saturation) measured with portable Oxygard Polaris Meter on site of water sample
Most of dissolved oxygen comes from atmosphere. Rapidly tumbling water as well as aquatic plants, algae. O2 levels rise from the morning reaching peak in afternoon due to photosynthesis.
Oxygen dissolves more easily in cooler water so climate is a major factor. During dry periods stream flow may be reduced, water levels lower reducing O2 levels.

## Slide 4: Dissolved Oxygen
Oxygen levels in incubation trays can vary depending the number of eggs, alevins, other organisms present, as they consume oxygen during cellular respiration, temperature, water flow and position in stacks.
Industry, fertilizers, waste and other sources of pollutants can also affect dissolved oxygen levels.
Levels less than 6mg/L or 6 ppm creates stressful conditions for spawning, less than 7 mg/L growth and 9 -12 mg/L supports abundant fish populations

## Slide 5: Temperature Affects
Amount of O2 Dissolved higher temp less O2
Rate of photosynthesis increases with increasing temp
Metabolic rates of aquatic organisms increases if Temp increases
Sensitivity of organisms to toxic wastes Amount of O2 Dissolved For example thermal pollution may cause fish to become more vulnerable to disease, due to stress of rising water temp or the resulting decrease in dissolved oxygen

## Slide 6: pH
pH is a measure of the H+ ion concentration or Acidity of the Water
Normal rain water around here is about pH 7-7.5 but is actually slightly acidic ( note ph of neutral water is around ph 7 depending on Temp.
absorption of CO2 carbon dioxide from the atmosphere and respiration product of organisms in the stream forms Carbonic acid making H20 slightly acidic
Changes in pH are very important to most organisms which adapt to a specific pH level and may die if changes even slight. pH 6.5-8 best for most
Higher acidity can cause heavy metal waste such as copper, mercury, lead and aluminum to corrode more easily releasing their ions into water (the toxic form). Heavy metals can accumulate on the gills of fish or cause deformities in young fish, reducing their chance of survival.

## Slide 7: Phosphates ( PO4-3 in ppm )
Phosphates is rapidly taken up by algae and larger aquatic plants. Phosphorus is a fundamental element in metabolic reactions of plants and animals.
Because algae need only small amounts of phosphorus to live, excess phosphates cause extensive algal growth called blooms. Algal blooms are classic symptoms of cultural eutrophication which is mainly human caused.
Cultural Eutrophication is human caused enrichment of water with nutrients. This promotes plant growth and decay which in turn causes biological oxygen demand limiting O2 for aquatic organisms. Human waste from wastewater treatment plants, septic systems, fertilizers, laundry and dish detergents, soaps, industrial waste, animal waste, decomposing organic matter all contribute.
Draining wetlands and marshes which act as filters for run off release nutrients like phosphorus.

## Slide 8: Nitrates ( NO3-) and Ammonia (NH3) in ppm
Nitrogen is an element necessary to all living plants and animals for building protein ( amino acids) Because Nitrates and ammonia acts a plant nutrient it can also cause eutrophication, promoting more plant growth and decay, which in turn increases biological oxygen demand limiting the amount of oxygen for aquatic organisms.
Sources of nitrates
Excretions of aquatic organisms are very rich in ammonia especially where ducks and geese are plentiful.
Sewage is the main source of nitrates added to waterways by humans, poorly functioning septic systems and inadequately treated sewage.
High levels of nitrates are sometimes found in groundwater beneath croplands due to excessive fertilizer use especially in heavily irrigated areas with sandy soils. Storm water runoff can carry fertilizers and animal feed lots including dairy. If not properly contained these wastes can seep into groundwater or transported as runoff into surface waters

## Slide 9: Turbidity( NTU in ppm)
Turbidity is a measure of the relative clarity of water: the greater the turbidity the murkier the water. Turbidity increases as the result of suspended solids (not soluble) that reduce the transmission of light. Suspended solids can range from clay, silt, plankton, industrial wastes and sewage.
At higher and prolonged levels of turbidity, water loses its ability to support a diversity of aquatic organisms. Water becomes warmer as suspended particles absorb heat from sunlight, causing oxygen levels to fall. Photosynthesis decreases due to less light.
Suspended solids can also clog fish gills, reduce growth rate, decrease resistance to disease, and prevent egg and larval development.
High turbidity can be caused by soil erosion, waste discharge, urban runoff, algae growth
Methods of measuring Turbidity – NEPHELOMETER – A DEVICE THAT MEASURES SCATTERING OF LIGHT
Transparency Tube with secchi Disc - this measures the depth of water through which one can see the bottom of the tube measured in cm

## Slide 10: Total Dissolved Solids (TDS in ppm)
Total dissolved solids are solids that are soluble in water and do not cause turbidity…in other words light can pass through without scattering. Imagine dissolving salt or sugar in water so its clear. That’s soluble.
Most dissolved solids in water include, soluble calcium salts, nitrates, bicarbonates, phosphates, sulphates and other dissolved ions. A specific level of these substances is essential for water balance living organisms because the level of many of these substances determines flow of water in and out of an organism’s cells. Notice your fingers if left in dishwater too long!
Mossom uses the Oakton Combo meter to measure TDS and Conductivity (as well as pH)

## Slide 11: Conductivity ( measured in uS micro seimens/cm)
Conductivity measures the ability of a water sample to conduct electricity. That means it must contain electrolytes which are basically soluble salts with ions free to move and cause a current to flow. As you are full of electrolytes… a reason not to plug in certain devices if you in H2O!
Basically the higher the conductivity the higher the concentration of dissolved solids like Soluble Salts. Road Salt run off is an issue that affects Aquatic life in fresh water creeks
(note that some soluble substances like sugar or ammonia are not electrolytes because not ions!)